R7: port6
R1: port3
R2: port8
S3 10.1.2.6/30
S0 10.1.2.5/30
e0 10.1.1.4/24
e0 10.1.1.3/24
Glacier: port2
VLAN 10

# Router 1
no ip domain-lookup
interface Loopback0
 ip address 10.1.1.1 255.255.255.0
 ipv6 address FEC0::1:1/112
interface Ethernet0/0
 ip address 10.10.10.3 255.255.255.0
 full-duplex
!
router eigrp 1
 network 10.0.0.0
 network 172.16.0.0
 no auto-summary
!
interface Serial0/0
 ip address 10.2.1.1 255.255.255.252
 encapsulation ppp
 service-module t1 clock source internal
 service-module t1 timeslots 1-24
!
int tunnel0
tunnel mode ipv6ip
tunnel source e0/0
tunnel destination 10.1.2.6
ipv6 add FEC0::13:1/112
# Router 7
no ip domain-lookup
interface Loopback0
 ip address 10.1.2.1 255.255.255.252
router eigrp 1
 network 10.0.0.0
 network 172.16.0.0
 no auto-summary
router eigrp 1
 network 10.0.0.0
 network 172.16.0.0
 no auto-summary
!
# Router 2

no ip domain-lookup
interface Loopback0
 ip address 10.1.3.1 255.255.255.0
 ipv6 address FEC0::3:1/112
router eigrp 1
 network 10.0.0.0
 network 172.16.0.0
 no auto-summary
router eigrp 1
 network 10.0.0.0
 network 172.16.0.0
 no auto-summary
!
interface Serial0/0
 ip address 10.2.1.2 255.255.255.252
 encapsulation ppp
 shutdown
 service-module t1 clock source internal
 service-module t1 timeslots 1-24
!
interface Serial1/3
 ip address 10.1.2.6 255.255.255.252
 clock rate 38400
!
int tunnel0
tunnel mode ipv6ip
tunnel source Serial1/3
tunnel destination 10.10.10.3
ipv6 add FEC0::13:3/112
# Glacier cisco WS-C3524-XL

interface FastEthernet0/17
 switchport access vlan 10
 no cdp enable
!
interface FastEthernet0/18
 description connection-to-GREEN-VLAN
 port monitor FastEthernet0/1
 switchport access vlan 10
 no cdp enable
!